## Slide 1: Activity A Design Project
Delivered by
Blue Group

## Slide 2: What will be covered in this presentation
Overview of the brief, our target market and their needs.
How our design meets the market need and how we have addressed environmental and inclusivity issues.
The materials chosen and the reasons for those materials.
The manufacturing method.
Overall summary.

## Slide 3: Overview of the brief, our target market and their needs
The brief:
  To design a new insulated mug for use by Bird watchers, taking into account environmental and inclusivity issues.
The target market:
  Bird watchers.
The targets needs:
  Keep contents hot for several hours.
  Spill proof.
  Neutral or camouflage exterior colour.
  Easy to use drinking orifice.
  Easy to transport.
  Durable.
  Resistant to the elements.

## Slide 4: Meeting Market, Environmental & Inclusivity Requirements
Market Needs
Keeping Contents Hot – Triple walled design
Spill Proof & Easy Transportation – Locking lid
Easy to Drink From – Extra wide opening
Neutral & Camouflaged – Wood Effect Finish
Durability – Dishwasher Safe Materials
(British Plastics Federation, 2021)
Environmental Requirements
All Materials are recyclable
Materials can be sourced from previously recycled sources.
Stainless Steel Stock Already 60% Recycled Material (BSSA, 2021)
BPA Free Plastic polypropylene is recyclable & suitable for food containers
  Alternative Lid Configuration Suitable for Adults with Mobility Disorders.
  Polypropylene can be heat sterilised without damage
Inclusivity
(Kidly, 2021)
Notes: Meeting Market, Environmental and Inclusivity Requirements
Market Needs:
Triple Walled construction with 2 vacuum insulated layers limit heat loss through convection and conduction
New twist locking lid design spill proof while closed and prevented from accidental opening, making suitable for transport in bags & backpacks
Extra wide drinking orifice to maximise liquid contact area with lips. Important part of the coffee drinking experience.
Wood Effect Wrap looks at home and camouflaged in woodlands environments
Stainless Steel Construction is resistant to acidic drinks & dishwasher safe.
Environmental:
Use of recycled and recyclable materials include Stainless Steel. Stainless steel on the market today already has an average recycled content of 60% according to the British Stainless Steel Association.
Polypropylene is recyclable and feedstocks can be sourced with already recycled content. (British Plastics Federation, 2021)
Inclusivity:
Alternative lid designs could be made available suitable for people with mobility disorders or problems swallowing. This style of lid is also non-spillable, but may be a less appealing style for general market.
References:
British Plastics Federation. (2021). Plastic Recycling. Retrieved July 24, 2021, from BPF.co.uk: https://www.bpf.co.uk/sustainability/plastics_recycling.aspx
British Stainless Steel Association. (2021). ENVIRONMENTAL ASPECTS OF STAINLESS STEEL. Retrieved June 24, 2021, from BSSA.org: https://bssa.org.uk/bssa_articles/environmental-aspects-of-stainless-steel/
Kidly. (2021). Non Spill Drinking Spout. Retrieved July 24, 2021, from Kidly.

## Slide 5: The materials chosen and reasons for those materials
18/8 Food grade
stainless steel
BPA free plastic
BPA free plastic
Travel mug design
Wood effect wrap

## Slide 6: Method of manufacture
Click to add text
Notes: Raw material:
18/8 food grade stainless steel sheet is cut into round plates to the required size/diameter for each of the mugs walled sections (inner, middle, outer)
Stretching:
A hydraulic punch is used to press/stretch the raw material into a rough shape of the mug design.
Shaping:
A large press is then used to follow the mug shaping guide, this ensures that the pits, size and shape meets the requirements for each of the inner, middle and outer mug sections.
Thread rolling/making:
A thread is machined into the top of the mug for the lid to be attached.
Assembly:
Each the of the inner, middle and outer sections of the mug are hydraulicly pressed together, with each section being leak tested and vacuumed using a vacuum machine to create the insulating between all the sections. The temperature and insulation is then tested.
Polishing:
Electrolysis polishing is used for the inner mug to ensure to improve the micro-geometry of the metal surface, reduce the surface roughness of the metal, so as to achieve the purpose of a bright and smooth surface.
Mechanical polishing is used on the outer bottle ensure it is smooth and the bottle mouth is smooth and bright. There must be no obvious drawing, scratching, black wire and pits. Once polishing is complete the mu is cleaned.
Pattern Printing:
The pattern design on the bottle is printed using thermal transfer printing and the wood effect wrap.
Lid manufacture:
The BPA free plastic will be injection molded to produce the parts of the lid and then fitted to the top of the mug.
Source:
Image - http://cdn.shopify.com/s/files/1/1823/7799/products/TeakwoodL_1024x.jpg?v=1603204405
Source:
(April 23rd, 2019, Kingstar) Manufacturing Process of Vacuum Insulated Stainless Steel Bottles , [Online].
available at:
https://www.waterbottle.tech/manufacturing-process-of-vacuum-insulated-stainless-steel-bottles/
This source contributed information explaining the manufacturing process for a vacuum insulated stainless steel bottle.